Z-Wave In-Wall On/Off Switch

| The GE ISZWWS!/45609 Z-Wave On/Off In-Wall Switch is part of a broad array of Z-Wave Lighting and Appliance components which provide convenience and flexibility to homeowners. Compatible with the Simon XT and Concord 4 (v4.5 and higher) home security systems, Z-Wave modules easily unify home electronics into an integrated wireless network without complicated programming. Z-Wave's modular design means devices can be easily added to a home network and can communicate wirelessly with other Z-Wave modules and remote controls. The Auto-Sensing feature automatically turns on lights and blue LED's allow you to quickly identify system status. Z-Wave also allows central control of various devices and the ability to command lighting and appliances from a web-based PC or cell phone. |  |
| --- | --- |

• Device can be turned on or off manually or via convenient Z-Wave remote control

• Blue LED indicates switch location for easy viewing in the dark

• Can be included in multiple groups and scenes

• Supports Advanced Configuration, LED status and invert switch

• Screw terminal installation with wiring connections for Line (Hot), Load, Neutral and Ground

• Uses standard-size wall plate for single gang installations

• White finish complements almost any décor

Power 120VAC, 60Hz

Signal (Frequency) 908.42 MHz

Load ratings: Incandescent -Minimum Load: 40W, Maximum Load: 600W

Motor – 1/2HP, Resistive – 1800W

Range: Up to 100 feet line of sight between the wireless controller and the closest Z-Wave receiver module.

Operating Temp. Range: 32–104° F (0–40° C)

For indoor use only.