Z-Wave Dual Outlet Wall Receptacle

| The GE ISZWWR1/45605 Z-Wave Dual Outlet Wall Receptacle is part of a broad array of Z-Wave Lighting and Appliance components which provide convenience and flexibility to homeowners. Compatible with the Simon XT and Concord 4 (v4.5 and higher) home security systems, Z-Wave modules easily unify home electronics into an integrated wireless network without complicated programming. Z-Wave's modular design means devices can be easily added to a home network and can communicate wirelessly with other Z-Wave modules and remote controls. The Auto-Sensing feature automatically turns on lights and blue LED's allow you to quickly identify system status. Z-Wave also allows central control of various devices and the ability to command lighting and appliances from a web-based PC or cell phone. |  |
| --- | --- |

• One Z-Wave remote-controlled AC outlet

• Remote ON/OFF control via the Z-Wave controller/network

• Manual ON/OFF control with the pushbutton

• Auto-Sensing* automatically turns light ON

• One always-ON pass-through AC outlet

• Blue LED indicates on/off status (supports advanced configuration for status)

• Z-Wave certified

* This feature is disabled by default. The Auto-Sensing feature must be enabled using the LCD Remote Control (IS-ZW-RC-1)

Power 120VAC, 60Hz

Signal (Frequency) 908.42 MHz

Maximum Load for the Z-Wave Controlled Outlet: 600W Incandescent,

½ HP Motor or 1800W (15A) Resistive

Maximum Load for Both Outlets: 1800W Resistive

Range: Up to 100 feet line of sight between the wireless controller and the closest Z-Wave receiver module.

Operating Temp. Range 32–104° F (0–40° C)

For indoor use only.