Z-Wave Outdoor AC Outlet Module

| The GE ISZWOM1/45604 Z-Wave Outdoor AC Outlet Module is part of a broad array of Z-Wave Lighting and Appliance components which provide convenience and flexibility to homeowners. Compatible with the Simon XT and Concord 4 (v4.5 and higher) home security systems, Z-Wave modules easily unify home electronics into an integrated wireless network without complicated programming. Z-Wave's modular design means devices can be easily added to a home network and can communicate wirelessly with other Z-Wave modules and remote controls. The Auto-Sensing feature automatically turns on lights and blue LED's allow you to quickly identify system status. Z-Wave also allows central control of various devices and the ability to command lighting and appliances from a web-based PC or cell phone. |  |
| --- | --- |

• One Z-Wave remote-controlled AC outlet

• Remote ON/OFF control via the Z-Wave controller

• Manual ON/OFF control with the pushbutton

• Auto-Sensing* automatically turns light on

• Weather- and impact-resistant housing for use outdoors in damp or wet conditions

• Integrated outlet cover keeps dirt and debris out when the module is not in use

• Z-Wave certified

Power 120VAC, 60Hz

Signal (Frequency) 908.42 MHz

Maximum Load for the Z-Wave Controlled Outlet: 600W Incandescent,

½ HP Motor or 1800W (15A) Resistive

Range: Up to 100 feet line of sight between the wireless controller and the closest Z-Wave receiver module.

Operating Temp. Range: 14–140° F (-10–60° C)

For outdoor use in dry, damp or wet locations.