Arming your Honeywell Security System

STAY Mode: Arms Perimeter Only, Entry Delay On

Used when you want to arm the system with persons staying inside (or if you have

pets that are moving throughout the premises).

The perimeter sensors are armed, but interior sensors are left disarmed.

Exit delay begins (you can leave through the entry/exit door, if desired).

An alarm sounds if any protected window or non-entry/exit door is opened.

You may otherwise move freely within the premises.

Persons entering later can enter through an entry/exit door, but they must disarm

the system within the entry delay period to avoid sounding an alarm.

NIGHT-STAY Mode: Arms Perimeter Only, Plus Selected Zones

Use NIGHT-STAY mode to provide increased security while staying inside.

Arms same as STAY mode, but also arms preselected interior sensors (programmed

by your installer), while other interior sensors are left disarmed.

Persons entering later can enter through an entry/exit door but they must disarm

the system and must not violate any of the programmed interior zones to avoid

sounding an alarm.

IMPORTANT: When NIGHT-STAY mode is on, the selected interior zones are

armed and cause an alarm if anyone enters those areas (e.g., waking in the middle

of the night). To avoid sounding an alarm, you must disarm the system before any

activity takes place in those interior zones.

INSTANT Mode: Arms Perimeter Only, Entry Delay Off

Used when staying inside and do not expect anyone to use an entry/exit door.

Arms same as STAY mode.

An alarm sounds immediately if any protected perimeter window or any door is

opened, including entry/exit doors.

IMPORTANT: Arming the system in this mode greatly increases the chance of

false alarms. Use extreme care in selecting this mode of arming.

AWAY Mode: Arms Entire System, Entry Delay On

Used when nobody will be staying inside (including pets).

The entire system (interior and perimeter) is armed.

Exit delay begins letting you leave through the entry/exit door.

An alarm sounds if a protected window or any door is opened, or if any movement

is detected inside your premises.

You can re-enter through an entry/exit door, but you must disarm the system

within the entry delay period to avoid sounding an alarm.

MAXIMUM Mode: Arms Entire System, Entry Delay Off

Used when leaving the premises for extended periods (e.g., vacation).

Arms same as Away mode, but entry delay is off.

An alarm sounds same as Away mode, and sounds upon opening entry/exit doors.

Arming the System (cont’d)

Arming Commands

Before arming, close all perimeter doors and windows, keep clear of all motion sensors and make sure the Ready to Arm

message is displayed.

Press these keys… Keypad Confirms By…

STAY MODE

Security code + 3 (STAY)

three beeps†

armed STAY message displayed

red ARMED indicator lights

NIGHTSTAY MODE

Security code + 3 (STAY) + 3 (STAY)

three beeps†

NIGHT-STAY message displayed

red ARMED indicator lights

INSTANT MODE

Security code + 7 (INSTANT)

three beeps†

armed STAY message displayed

red ARMED indicator lights

Note that entry delay is turned off.

AWAY MODE

Security code + 2 (AWAY)

Two beeps†, or, if programmed, beeping for

duration of exit delay

armed AWAY message displayed

red ARMED indicator lights

Leave the premises through an entry/exit

door during the exit delay period to avoid

causing an alarm. The keypad beeps

rapidly during the last 10 seconds of the

exit delay to warn you that it is ending.

MAXIMUM MODE

Security code + 4 (MAX)

same as AWAY (described above)

Note that entry delay is turned off.

† Arming Ding: In addition to the keypad beeps, the external sounder emits a short “ding” sound after arming, if

programmed to do so. The ding confirms that the system is armed, and may occur immediately after the command or be

delayed (until arm/disarm report is sent or exit delay expires). Ask your installer about how this feature is set for your system.

QUICK ARMING

If "Quick Arming" was programmed by the installer, the [#] key can be pressed in place

of the security code when arming the system in any of the arming modes (except Night-

Stay). However, the security code must always be used when manually disarming the system.